## Slide 1: Live in the Express Lane
Patrick Jahnke*§, Vincent Riesop§, Pierre-Louis Roman┼, Pavel Chuprikov ┼, and Patrick Eugster* ┼▲
*TU Darmstadt, §SAP, ┼Università della Svizzera italiana, ▲Purdue University
Notes: Hello everybody and welcome to the presentation of our work live(leif) in the express lane I’m Patrick Jahnke and this work was in cooperation with Vincent Riesop, Pierre-Louis Roman, Pavel Chuprikov, and Patrick Eugster

## Slide 2: Crucial challenges of coordination tasks
Transition in the last decade
    Conceived as distributed (cloud-based) application
    Data center (DC) interferences prevent predictability
    Weak synchrony assumptions to guarantee safe execution
Mitigation of interference in DCs to accelerate distributed systems (DSs)
    Awareness of timely sensitive interactions
    Tight upper bounds required
    Foundation to increase performance of DS coordination tasks
Notes: In the last decade, a tremendous increase in Internet connectivity and the need for more computational performance changed the way we conceive applications. Today, most new applications are conceived as distributed, and in particular cloud-based, applications.
Most distributed system designs treat the underlying infrastructure as a generic communication system. One of the main issues with this abstraction is the longstanding problem of interference of concurrent interactions and thus unpredictable latency of commodity networks and hosts.
Many applications and components have been designed to cope with the unpredictability of the infrastructure by making weak synchrony assumptions to guarantee a safe execution of their protocol.
They rely on upper bounds for the latency of their interactions to ensure liveness, by defining timeouts, and as thus benefit strongly from interactions with low latency and bounded jitter.
Therefore, one of the main challenge in terms of performance of a DS is to mitigate interference in data center commodity systems.
To do so it is important to get a better understanding and awareness of timely sensitive interactions and tighten upper processing and communication bounds for practical purposes.
This would solve the longstanding problem of the unpredictability of transmission and processing times for individual packets and, in particular asynchronous behavior of commodity networks and hosts which is the foundation to increase the performance of DS coordination tasks like Failure detection and consensus which are wide spreaded in practice.

## Slide 3: Related work
Low latency
    Generic approaches
    99th percentile
    No process response time
[1] M. P. Grosvenor, M. Schwarzkopf, I. Gog, R. N. M. Watson, A. W. Moore, S. Hand, and J. Crowcroft. Queues Don’T Matter when You Can JUMP Them! In: USENIX NSDI. 2015, pp. 1–14. [2] B. Montazeri, Y. Li, M. Alizadeh, and J. K. Ousterhout. Homa: A Receiver-Driven Low-Latency Transport Protocol Using Network Priorities. In: ACM SIGCOMM. 2018, pp. 221–235. [3] J. Perry, A. Ousterhout, H. Balakrishnan, D. Shah, and H. Fugal. Fastpass: A Centralized "Zero-Queue" Datacenter Network. In: ACM SIGCOMM. 2014, pp. 307– 318. [4] G. Prekas, M. Kogias, and E. Bugnion. ZygOS: Achieving Low Tail Latency for Microsecond-Scale Networked Tasks. In: ACM SOSP. 2017, pp. 325–341. [5] H. T. Dang, D. Sciascia, M. Canini, F. Pedone, and R. Soulé. NetPaxos: Consensus at Network Speed. In: SIGCOMM SOSR. 2015, pp 5:1–5:7. [6] Z. István, D. Sidler, G. Alonso, and M. Vukolic. Consensus in a Box: Inexpensive Coordination in Hardware. In: USENIX NSDI. 2016, pp 425–438. [7] A. Basu, B. Charron-Bost, and S. Toueg. Simulating Reliable Links with Unreliable Links in the Presence of Process Crashes. In: WDAG. 1996, pp 105-122.
In network processing
    Specific to particular service
    Specific hardware required
    No process response time
[1, 2, 3, 4]
[5, 6]
Communication links are reliable but asynchronous [7]
Notes: Current related work can be categorized in two areas:
The first one is focusing on low latency. The works in this area decrease the latency for all types of traffic but considering in there evaluation usually the 99th percentile.
Furthermore, there are pure transmission times and throughput considered but no processing time.
The other category is focusing on network support for very specific tasks or to a particular service.
They have usually special hardware requirements but do not consider endhosts and its processing time.
Overall, the common understanding is that communication links are reliable but asynchronous.

## Slide 4: Features of X-Lane
  Interference free environment
    Bounded communication latency / jitter
    Bounded processing latency / jitter
  Generic design
    Supports multiple coordination protocols
    Commodity and specialized hardware
Notes: The idea behind the express lane or X-Lane for short, is an interference-free environment for selected interactions with ultra low latency and bounded jitter for communication AND processing. The remaining interactions follow common design principles.
Even if in this work we are focusing on coordination traffic of DSs and show the benefits for asynchronous algorithms of bounded communication and processing latency.
We designed X-Lane in a generic fashion to support different types of coordination protocol and it should be executable on commodity and new generation of DC hardware.

## Slide 5: Separation between X-Lane & regular system
  X-Lane isolated from “regular system”
  Prioritize X-Lane packets to prevent losses
  Process communication over bridges
Notes: To realize an interference-free environment we isolate X-Lane with its services from the regular system since processes of the regular system have to deal with shared processor time.
This resource sharing introduces unpredictable jitter for those processes while critical interactions need an upper bound for certain tasks.
In the network, X-Lane prioritize its packets to prevent packet losses due to buffer overflows.
To communicate from the regular system to X-Lane and vise versa, X-Lane provides two sets of queues, called bridges, here visualized as cuboid, to establish the interface between processes in X-Lane and on the regular system. The express-to-regular bridge in green grants write access to X-Lane, which is the green parallelogram and read access to the regular system, here in blue.; inversely for the regular to X-Lane bridge, visualized as the blue cuboid.
Bridges are addressable using direct memory access (DMA) but are placed at different locations depending on the endhost HW available.
CLICK

## Slide 6: Usual workflow for a packet
Notes: What we see here is a very common example of the workflow for a communication between two applications in this case application 1 running at Core A.X on host A andthe corresponind application 1 running at Core B.Y on host B.
So lets go through all sources of jitter that might effect the latency:
CLICK For an application that shares resources with other applications the operating system has to handle the sharing with a scheduler. Also an idle state or frequency scaling of a core introduce execution delays for the application.
Once the application has the execution handler from the scheduler the application can start to process data and creating a packet. Than it has to go through the kernel more or less extensive - I come to that point in a minute.
but in this case the packet goes through the protocol stack and the NAPI driver and the device specific driver.
CLICK
All processing steps can be interrupted by many diffenrent things like iterrupt request, tick timer, read copy update watchdog, non makable interrupts and system mode interrupts.
CLICK
Then we also have to consider that the core and the NIC are at the same NUMA node. Otherwise we would introcude QPI traffic.
CLICK
Once the packet is transfered to the NIC, the NIC has its own buffers which migth be occupied and therefore queuing latency can be introduced.
CLICK
On the switch or switches depending on the number of hops, queuing latency can be also introduced and since we have a very limited number of dedicted per port memory and also limited shared memory over all ports the packet might be dropped if the queues are already full.
CLICK
On the receiving side we have basically the same steps.
The only difference is that usually you have to raise an interrupt that the host system copies the packet from the NIC to the host.
As mentioned before with techniques like DPDK you are able to prevent certain steps in the kernel...
CLICK
...especially at the protocol layer.
CLICK

## Slide 7: Usual workflow for a packet
Notes: What we see here is a very common example of the workflow for a communication between two applications in this case application 1 running at Core A.X on host A andthe corresponind application 1 running at Core B.Y on host B.
So lets go through all sources of jitter that might effect the latency:
CLICK For an application that shares resources with other applications the operating system has to handle the sharing with a scheduler. Also an idle state or frequency scaling of a core introduce execution delays for the application.
Once the application has the execution handler from the scheduler the application can start to process data and creating a packet. Than it has to go through the kernel more or less extensive - I come to that point in a minute.
but in this case the packet goes through the protocol stack and the NAPI driver and the device specific driver.
CLICK
All processing steps can be interrupted by many diffenrent things like iterrupt request, tick timer, read copy update watchdog, non makable interrupts and system mode interrupts.
CLICK
Then we also have to consider that the core and the NIC are at the same NUMA node. Otherwise we would introcude QPI traffic.
CLICK
Once the packet is transfered to the NIC, the NIC has its own buffers which migth be occupied and therefore queuing latency can be introduced.
CLICK
On the switch or switches depending on the number of hops, queuing latency can be also introduced and since we have a very limited number of dedicted per port memory and also limited shared memory over all ports the packet might be dropped if the queues are already full.
CLICK
On the receiving side we have basically the same steps.
The only difference is that usually you have to raise an interrupt that the host system copies the packet from the NIC to the host.
As mentioned before with techniques like DPDK you are able to prevent certain steps in the kernel...
CLICK
...especially at the protocol layer.
CLICK

## Slide 8: X-Lane workflow for commodity hardware
Notes: With X-Lane on commodity hardware we cut one core out of the rest of the system and disabled all possible sources of jitter.
The core is running on max frequency all time and while the IRQ can be handled by other cores, the tick timer has to be blocked during the X-lane excution. The other effects are disabled.
X-lane is implemented as kernel module. Therefore we designed the bridges between asynchronous User Space or rest of the system and X-Lanes kernel module.
The kernel module interacts with the NIC driver directly.
The X-lane core obiously is running on the same numa node as the nic.
On the NIC we created a dedicated buffer for X-lane.
Same on the switches where we used the strict priority technique with a dedicated X-lane queue which has the highest priority.
On the receiving side we also defined a dedicated receiving buffer for X-lane on the NIC.
After receiving a packet the NIC raise an interrupt on the endhost.
To estimate the latency we created a traffic engineering optimization algorithm that also take care that the queues are not oversubscribed.
X-lane has also a control mechanism to share the resources and timings through the system.
CLICK
OLD:
Here we set a so called optimitical timestamp and lock basically all requests from the application until the packet payload is received and analyzed.
Then X-lane provides the new data at the shared memory buffer available for the rest of the system.

## Slide 9: X-Lane workflow with smartNICs
Notes: We also implemented X-Lane on new NIC generations so called smartNICs, more concretly on Netronomes smartNICs. (NFP-4000)
With this design we offload the X-Lane kernel module down to the NIC.
Therefore, other system modifications are not needed anymore.
But we still using the bridges but now between NIC and main CPU and also using the control mechanisms explained before…
CLICK

## Slide 10: Latency and jitter for DPDK, QJump and X-Lane
Notes: We now present a heartbeat failure detector which we implemented with X-Lane:
We run the experiments over 21 days but the plots here are just cutouts with the highes jitter point.
All graph are visualized in the same way with number of packets on the x axis and latency on the y axis.
With X-Lane on commodity hardware we dont really see outliers anymore and the jitter is around 650 ns.
The jitter is mostly comming from the PCIe bus because if we run X-lane on the smartNIC we see even more stable jitter.
CLICK
We compared the different X-lane implementations with DPDK which is as discussed before the foundation for a lot of related work in the area of traffic optimization and QJump.
As you can see DPDK and QJump have outliers in the double digit millisecond range…
CLICK
…so please consider the different scales for the latency on the y axis.
CLICK

## Slide 11: Tail latency over 21 days
Notes: We see here the latency on the y axis and different percentiles on the x axis.
Please consider the log scale on the y axis.
Here we also visualize X-lane zero which is the same code but without a dedicated core on endhosts.
If we now consider the distribution of the different approaches we see that X-lane was over the whole experiment very stabel while DPDK and QJump is having multiple jumps which makes it hard to define upper bound on latency.
This is propably also the reason why other approaches in this field consider only 99th percentile even if they talk about bounded latency.
CLICK

## Slide 12: Latency and throughput results for Raft implementations
Notes: Now we also implemented the Raft protocol on X-Lane called X-Raft. We compared it with etcd and Redis which doesnt use a strong consitency state replication mechanism. And we where able by changing 20 lines of redis code using X-Raft below.
What we see at the plot is the average latency for writing on the y axis and distributing on value over increasing number of processes on the x axis to show the scalability.
On the right hand side we see the average throughput of MB/s on the y axis ans also with increasing numbers of processes on the x axis.
We see that X-Raft perfoms best and even better than a replication mechanism without strong consitency.
CLICK

## Slide 13: Conclusion
Low latency and jitter for coordination interaction
X-Lane isolated from regular system
Generic system design
Commodity software / hardware and smartNIC support
Notes: To conclude X-Lane provides an interference environment for low latency and jitter for coordination traffic.
X-Lane is isolated from regular system but is able to communicate to the regular system over bridges.
It has a generic system design to accelerate different types of interactions and is executable on Commodity software / hardware and also on smartNIC's.
CLICK

## Slide 14: Interested? Questions? Thank YOU!
Notes: With this I’m finish with the presentation of our work on X-Lane and thank you for your attention and now I'm happy to answer your questions.
Thank you